## Slide 1: Introduction
The purpose of this document is to instruct users how to use the code described by Berry et. Al.
This code will calculate:
  Angle With Respect to Horizontal
  Sagittal Cobb Angle
  Superior (L1-L3) Cobb Angle
  Inferior (L4-S1) Cobb Angle
  Intervertebral Angle
    Sagittal
    Coronal
    Axial
  Intervertebral Height
    Anterior
    Center
    Posterior

## Slide 2: OsiriX
Osirix is an open source software that is commonly used to view medical images
Osirix can be downloaded from http://www.osirix-viewer.com/Downloads.html
Download the “Export ROIs” Plugin in Osirix at Plugins->Plugins Manager->Available Plugins->Export ROIs

## Slide 3: Seeding Sagittal ROIs
Import Scans into Osirix (Import)
Select Copy Links
Double-Click image to open it
Select Point tool in region of interest toolbox

## Slide 4: Seeding Sagittal ROIs
Place points on the corners of each vertebrae
Double click each point to rename
Naming system is as follows
  L3-1
Lumbar (L) or Sacrum (S)
Level
1 - Anterior/Superior
2 - Posterior/Superior
3 - Posterior/Inferior
4 - Anterior/Inferior

## Slide 5: Seeding Sagittal ROIs
Seed all images in stack. If vertebrae is not present, do not seed
Save ROIs
  ROI->Save all ROIs of this Series
Export ROIs
  Plugins->ROI Tools->Export ROIs->Export as .csv
File Naming Convention
  LS001_Sag_P1
Lumbar Spine
Subject Number
Sagittal (Sag) or Axial (Axi) points
Position

## Slide 6: Seeding Axial ROIs
Right click on the current image to open a second window
Under Orientation, click the axial orientation icon
Select like points on the pedicle of each vertebra. Points are named: L5-L
Save and export ROIs following previously defined naming convention
Lumbar (L) or Sacrum (S)
Level
Left (L) or Right (R)

## Slide 7: Seeding Axial ROIs

## Slide 8: Saving Files for Analysis
Folder: Measurements
Folder: Sagittal
Folder: Axial
Files
LS001_Sag_P1.csv
LS001_Sag_P2.csv
LS002_Sag_P1.csv
LS002_Sag_P2.csv
.
.
.
Files
LS001_Axi_P1.csv
LS001_Axi_P2.csv
LS002_Axi_P1.csv
LS002_Axi_P2.csv
.
.
.
Note: You must have the same number of files in each folder

## Slide 9: Matlab
Open Main.m
Change the following parameters in the top of the file
ipres: in-plane resolution
thk: slice thickness
num_subjects: number of subjects
num_positions: number of positions measured
displayflag: display images Yes (1) or No (0)
writedataflag: write file Yes (1) or No (0)

## Slide 10: Matlab
Run Main.m
A GUI will open, navigate to and select the location where the sagittal .csv files are located and select a file
Another GUI will open, navigate to and select the location where the axial .csv files are located and select a file